## Slide 1: University of Maryland Baltimore County Department of Computer Science and Electrical Engineering CMPE 212 Laboratory (Discussion 2)
Hasibul Hasan
ha26@umbc.edu
Ankit Baingane
ankitb1@umbc.edu
Edward Hanson
ehanson1@umbc.edu
* Most of the slides are courtesy of previous TA: Rashidul Islam and Patrick Sykes

## Slide 2: An Introduction to Verilog
Hardware Description Language (HDL)
Basic idea is a programming language to describe hardware
Initial purpose was to allow abstract design and simulation
  Design could be verified then implemented in hardware
Now Synthesis tools allow direct implementation from HDL code.
  Large improvement in designer productivity

## Slide 3: What is Verilog?
A hardware description language (HDL) to describe:
    Wires
    Registers
    Connection to Registers
    Clock Pulses
Verilog is NOT an object oriented language
Verilog uses “modules” instead of functions and methods

## Slide 4
Verilog is a Hardware Description Language.
Syntax is similar to C.
Modular implementation of circuit components:
  Modules form the building blocks of circuit components.
  Bigger modules are made up of smaller modules.
2 different ways to program (“Levels of Abstraction”):
  Behavioral
  Structural …more on these later
What is Verilog?

## Slide 5: Hardware Description Language
HDL: Programming language used to describe the behavior of an electronic circuit.
Uses simulations to test and verify a circuit’s functionality.
Difference between HDL’s and other programming languages: HDL’s include a notion of time.

## Slide 6: Syntax
White spaces are ignored.
Commenting:
  // single line
  /* multiple line */
Variables:
  Must start with an alphabet char, or an underscore followed by an alphabet char.
  Case sensitive.

## Slide 7: Keywords: ‘reg’ and ‘wire’
Register
  Represents storage elements (memory).
  Holds value until next assignment.
  reg [7:0] test;
  // a 8-bit register vector
  // individual bits: test[7], ..., test[0]
Wire
  Represents physical wires that connect modules.
  Does not store values, must be continuously driven.
  wire [15:0] net1;
    // a 16-bit wire vector (aka ‘net’)
    // individual bits: net1[15], ..., net1[0]

## Slide 8: Keywords: ‘input’ and ‘output’
Input
  Understood as a special ‘wire’ that brings input values into a module.
  Can be read from, unlike normal wires.
  input [7:0] in1;
Output
  Understood as a special ‘wire’ that drives output values from a module.
  Even though it is a wire by default, it can be assigned like a register under certain circumstances.
  output [7:0] out1;

## Slide 9: Modules
Most basic unit of hierarchy in Verilog
Can be a single circuit element, or a collection of lower level modules connected together.
Contained in 1 Verilog file.
Multiple modules can reside in 1 file, but this is not recommended.
Module name should match the file name. So the module ‘adder’ would reside in the file named ‘adder.v’.

## Slide 10: Modules continued
Defining a module:
  module <module_name>(<module_terminal_list>);
  ...
  <module internals>
  ...
  endmodule
Defining a Half Adder module:
  module HalfAdder(A, B, S, Cout);
  ...
  <functionality of Half-Adder>
  ...
  endmodule
We can describe the functionality of a module with either Structural code or Behavioral code.

## Slide 11: 2 Levels of Abstraction
Structural code
Represents circuit components.
  Gates
  Lower level modules
May use Verilog’s Gate Primitives:
  and u1(y, a, b);
  Instantiates an AND gate called u1 with inputs a and b, and output y.
Behavioral code
No direct mapping to circuit components.
  Loops
  if-else statements
May use Verilog’s Boolean operators:
  assign y = a && b;
  Performs the AND operator on a and b, and assigns the result to y.

## Slide 12: 2 Levels of Abstraction
Structural: Gate Primitives
Predefined in Verilog. Can have multiple inputs.
and and_1 (out, in0, in1);
nand nand_1 (out, in0, in1,in2);
or or_1 (out, in0, in1);
nor nor_1 (out, in0, in1, in2, in3);
xor xor_1 (out, in0, in1, in2);
xnor xnor_1 (out, in0, in1);
Behavioral: Operators
Bitwise: ~, &, |, ^
Logical: !, &&, ||
Reduction: &, |, ^
Arithmetic: +, -,*, /, **
Relational: >, >=, ==, !=
Shift: >>, <<

## Slide 13: Module Example – Structural
module fred(O,A,B,C);
input A,B,C;
output O;
wire W;
or (W,B,C);
and (O,A,W);
endmodule

## Slide 14: Module Example – Behavioral
module fred(O,A,B,C);
input A,B,C;
output O;
wire W;
assign W = B | C;
assign O = A & W;
endmodule

## Slide 15: Testbench
A testbench tests the functionality of a module.
Always contains behavioral code.
Controls the inputs to a module, and examines the outputs of a module.
A testbench for the Fred module:
  Instantiates a Fred module, and gives this instance a name.
  Applies all the different possible combinations of A, B, and C to the module’s inputs.
  Displays the output values so that you can see if the Fred module is working as expected.

## Slide 16: Module Example – Test Bench
module testbench4Fred();
reg [2:0] switches;
wire y;
fred f1(y,switches[2], switches[1], switches[0]);
initial
begin
switches = 000;
$display(“switches=ABC\n”);
#80 $finish;
end
always
begin
switches = switches + 001;
#10 $display(“switches=%b, y=%b”, switches, y);
end
endmodule

## Slide 17: How to Compile / Run Verilog files
Log onto a computer with linux.
In a command window, enter:
  verilog <testbench name> <module name>
Make sure you are in the same folder as the files which you wish to run.
If you’re not in the same folder, specify the file paths in front of the testbench name and module name.
You can append as many modules to this command as you wish, but use one testbench at a time.

## Slide 18: Remote Linux Access
For windows, download putty
http://the.earth.li/~sgtatham/putty/latest/x86/putty.exe
  Open the exe (don’t need to install). The Host Name is “gl.umbc.edu” and the Connection type is SSH.
  Enter your UMBC username and password.
For Mac/Linux users, open terminal and type “ssh gl.umbc.edu”.
  Enter your UMBC username and password.

## Slide 19: Some Useful Linux Command
  ls //List contents of current directory
  clear //Clear the screen
  cd <directory name> // Navigations between folders
  cd .. // Takes you out from current folder
  mkdir <directory name> // Create a New Folder
  find // Search for files matching certain patterns
  cat> <file_name.filetype> // Create new file e.g. cat>half_adder.v
  cat <file_name.filetype> // To see output of files
  Always search in Google
  Use “Tab” button of keyboard
  Editor: nano, emacs

## Slide 20: Running Verilog for the 1st time
SSH into UMBC's gl server through Putty
Type the following commands:
cd nano .cshrc
Go to the bottom and find the last line with an "endif" on it. Below this line, type:
source /afs/umbc.edu/software/cadence/etc/setup_2008/cshrc.cadence
Save this file (ctrl-x ctrl-s), then exit nano (ctrl-x ctrl-c).

## Slide 21: Running Verilog for the 1st time
Type the following commands, don’t forget the ‘dot’ at the end of each command:
cp /afs/umbc.edu/software/cadence/etc/setup_2008/cds.lib .
cp /afs/umbc.edu/software/cadence/etc/setup_2008/hdl.var .
cp /afs/umbc.edu/software/cadence/etc/setup_2008/.cdsinit .
cp /afs/umbc.edu/software/cadence/etc/setup_2008/.simrc .
source ~/.cshrc
Verify that Verilog is installed by performing the following command:
which Verilog
If there is no error, you are ready to use verilog

## Slide 22: Half Adder Module in Verilog & Verification
Combinational arithmetic circuit that adds two numbers
Output: a sum bit (S) and a carry bit (C)
Disadvantage: Only add two input bits and neglect carry
Binary addition process is not complete and that’s why it is called half adder

## Slide 23: Half Adder Module in Verilog & Verification
AND Gate
X
Y
Z
Z = X & Y
X Y Z
0 0 0
0 1 0
1 0 0
1 1 1

## Slide 24
Exclusive – OR (XOR) Gate
X Y Z
X
Y
Z
0 0 0
0 1 1
1 0 1
1 1 0
Z = X ^ Y
Half Adder Module in Verilog & Verification

## Slide 25: Verilog Guides
Free online tutorial: http://www.ece.umd.edu/class/enee359a.S2008/verilog_tutorial.pdf
Verilog Quick reference: http://www.stanford.edu/class/ee183/handouts_win2003/VerilogQuickRef.pdf

## Slide 26: Reminder !!!
Send your group info to-
ha26@umbc.edu
Name and email address of each member
One email from each group
Send these information by tonight