## Slide 1: University of Maryland Baltimore County Department of Computer Science and Electrical Engineering CMPE 212 Laboratory (Discussion 3)
Hasibul Hasan
ha26@umbc.edu
Ankit Baingane
ankitb1@umbc.edu
Edward Hanson
ehanson1@umbc.edu

## Slide 2: Making Full Adder using Two Half Adders in Verilog

## Slide 3: Making Full Adder using Two Half Adders in Verilog
Half adder module:
module ha(Sum,Carry,A,B);
input A,B;
output Sum,Carry;
assign Sum=A^B;
assign Carry=A&B;
endmodule

## Slide 4: Making Full Adder using Two Half Adders in Verilog
Full adder module:
`include "Half_Adder.v"
module fa(Sum,Cout,A,B,Cin);
input A,B,Cin;
wire W1,W2,W3;
output Sum,Cout;
ha f1(W2,W1,A,B);
ha f2(Sum,W3,W2,Cin);
assign Cout=W1|W3;
endmodule

## Slide 5: Making Full Adder using Two Half Adders in Verilog
Full adder Testbench:
module fa_tb();
reg[2:0] in;
wire Sum,Cout;
fa function1(Sum,Carry,in[2],in[1],in[0]);
initial
begin
in = 3'b000;
repeat(7) #50 in=in+1'b1;
end
initial
$monitor(" A=%b B=%b Cin=%b ---> Sum=%b Cout=%b",in[2],in[1],in[0],Sum,Carry);
endmodule

## Slide 6: Making Full Adder using Two Half Adders in Verilog
Output:
A=0 B=0 Cin=0 ---> Sum=0 Cout=0
A=0 B=0 Cin=1 ---> Sum=1 Cout=0
A=0 B=1 Cin=0 ---> Sum=1 Cout=0
A=0 B=1 Cin=1 ---> Sum=0 Cout=1
A=1 B=0 Cin=0 ---> Sum=1 Cout=0
A=1 B=0 Cin=1 ---> Sum=0 Cout=1
A=1 B=1 Cin=0 ---> Sum=0 Cout=1
A=1 B=1 Cin=1 ---> Sum=1 Cout=1

## Slide 7: Hardware Implementation of a Full Adder Circuit

## Slide 8
Hardware Implementation of a Full Adder Circuit
IC no. | Description
7400 | quad 2-input NAND gate
7402 | quad 2-input NOR gate
7404 | hex INVERTER
7408 | quad 2-input AND gate
7432 | quad 2-input OR gate
7486 | quad 2-input XOR gate
IC part no. of the logic gates:

## Slide 9: Hardware Implementation of a Full Adder Circuit
Pinouts of IC 7408,7432, and 7486:

## Slide 10
  Counting pin no. of DIP Ics:
Hardware Implementation of a Full Adder Circuit
For any IC, find its datasheet online.
  e.g. http://alldatasheet.com/

## Slide 11
Placing ICs in a breadboard:
Hardware Implementation of a Full Adder Circuit

## Slide 12
Placing ICs in a breadboard:
Hardware Implementation of a Full Adder Circuit

## Slide 13
DIP switch:
  Used for giving inputs to the logic circuits.
  Connect one end to the ground and the other to the input pin of your ICs.
  Important: Switching ON the DIP switch will simply close the switch.
    If connected to power, switch on is giving input ‘1’
    If connected to ground, switch on is giving input ‘0’
Hardware Implementation of a Full Adder Circuit

## Slide 14
LEDs:
  Used for observing the output of the logic circuits.
Hardware Implementation of a Full Adder Circuit
Always use with a resistor in series
Use multimeter in case you can’t find the longer leg out.

## Slide 15: Hardware Implementation of a Full Adder Circuit
Schematic-

## Slide 16: Bad News !!!
Your first Lab assignment is due next Friday, 29th Sep
You’ll be given a combinational logic circuit-
  You need to verify its truth table using Verilog.
  Implement it with hardware.

## Slide 17: Questions?

## Slide 18: Multimeter

## Slide 19: Power Supply
Adjust Voltage or Current?
Adjust knob
Resolution select keys
Output On/Off key
Meter selection keys
Power Supply Outputs