## Slide 1
University of Maryland Baltimore County Department of Computer Science and Electrical Engineering CMPE 212 Laboratory (Discussion 8)
Hasib Hasan
ha26@umbc.edu
Edward Hanson
ehanson1@umbc.edu
Ankit Baingane
ankitb1@umbc.edu
Notes: 1

## Slide 2
Lab assignment due today !!!
You’ll be given problems similar to Lab 07.
  You need to display required number / letter/ character according to the given conditions.
  Make truth table for each segment from the given conditions.
  Find the expressions for each segment from the truth table using K-map or any other technique.
  Build your circuit and display the characters for different input conditions as described by the problem.

## Slide 3
Interfacing 7-segment display
Attention !!!
  Please use separate RESISTORS in series before each segment.
    Use resistors of 1k or 330 Ohms.

## Slide 4
Interfacing 7-segment display

## Slide 5
Interfacing 7-segment display
Attention !!!
  NEVER test your LED / 7-segment display by connecting to the power.
  Use your Multimeter to check if they’re working.
    Take your dial to continuity/diode mode.
    Connect the Black lead of the multimeter to pin no. 4 or 12 and the Red lead to other pins.
    If the segment lights up or the multemeter displays a value, it’s working.

## Slide 6
Interfacing 7-segment display
Pro tip:
Don’t connect any pin of the display directly to the DIP switch with/without a resistor.
  Example: f = A

## Slide 7
Interfacing 7-segment display
What you would like to do:
f=A

## Slide 8
Interfacing 7-segment display
Problem:
  The DIP switch doesn’t supply power to the display like the ICs do. So, it won’t work at all.

## Slide 9
Interfacing 7-segment display
What you need to do:
  Use the logic A.A=A or A+A=A or
  This way, the output comes from an IC that can supply power to the display.

## Slide 10
Interfacing 7-segment display
f=A

## Slide 11
Interfacing 7-segment display
f=A

## Slide 12
Interfacing 7-segment display
f=A

## Slide 13
Interfacing 7-segment display
  Other notes:
    Refer to all previous slides for the IC pinouts and debugging of the circuit.
    Don’t give power supply before completing the circuit.
    Check again for the 7-segment displays if they’re connected to a resistor.

## Slide 14
Questions?
Notes: 14

## Slide 15
Notes: 15