## Slide 1: University of Maryland Baltimore County Department of Computer Science and Electrical Engineering CMPE 212 Laboratory (Discussion 9)
Hasib Hasan
ha26@umbc.edu
Ankit Baingane
ankitb1@umbc.edu
Edward Hanson
ehanson1@umbc.edu

## Slide 2: Multiplexers
Also called MUX
A device that selects one of several analog or digital input signals and forwards the selected input into a single line.
The device in the counterpart is called Demultiplexer (DEMUX)

## Slide 3: Multiplexers
Uses:
Communication System – Increases the efficiency of the communication system by allowing the transmission of data, such as audio & video data from different channels via through a single line.
Computer Memory – Used in computer memory to keep up a vast amount of memory in the computers, and also to decrease the number of copper lines necessary to connect the memory to other parts of the computer.
Telephone Network – Used in telephone networks to integrate multiple audio signals on a single line of transmission.
Bottom line: Economizing connections or channels

## Slide 4: Multiplexers
Digital MUX:
The selector lines have digital values.
No. of input signals could be .
If no. of input channels is , no. of selector lines is ‘n’
Named as ‘

## Slide 5: Multiplexers
Digital MUX: What’s inside?
  Made of combinational logic
Truth table: (for 2x1 MUX)
S | D1 | D0 | Out
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
D0 + SD1

## Slide 6: Multiplexers
Expressions for the output:
  2x1 MUX: D0 + SD1
  Similarly:
4x1 MUX:
8x1 MUX ??
0
1
Notice-
00
01
10
11

## Slide 7: Multiplexers
Circuit:
2 x 1 MUX
4 x 1 MUX
8 x 1 MUX

## Slide 8
3-input AND gate IC:
IC 7411

## Slide 9: Multiplexers
Implementation in Verilog: 2x1 MUX module
Notice: ‘case’ statement
module mux_2(out,i1,i2,sel);
input sel;
input i1,i2;
output out;
reg out;
always @(sel or i1 or i2)
begin
case (sel)
1'b0: out=i1;
1'b1: out=i2;
endcase
end
endmodule

## Slide 10: Multiplexers
Implementation in Verilog:
  testbench script-
module mux_2_tb();
reg[2:0] in;
wire out;
mux_2 function1(out,in[0],in[1],in[2]);
initial
begin
in=3'b000;
repeat(7) #50 in=in+1'b1;
end
initial
$monitor(" Selector=%b Channel2=%b Channel1=%b Output=%b",in[2],in[1],in[0],out);
Endmodule

## Slide 11: Multiplexers
Implementation in Verilog:
  Output:
    Selector=0 Channel2=0 Channel1=0 Output=0
    Selector=0 Channel2=0 Channel1=1 Output=1
    Selector=0 Channel2=1 Channel1=0 Output=0
    Selector=0 Channel2=1 Channel1=1 Output=1
    Selector=1 Channel2=0 Channel1=0 Output=0
    Selector=1 Channel2=0 Channel1=1 Output=0
    Selector=1 Channel2=1 Channel1=0 Output=1
    Selector=1 Channel2=1 Channel1=1 Output=1

## Slide 12: Questions?