## Slide 1
University of Maryland Baltimore County Department of Computer Science and Electrical Engineering CMPE 212 Laboratory (Discussion 12)
Hasib Hasan
ha26@umbc.edu
Edward Hanson
ehanson1@umbc.edu
Ankit Baingane
ankitb1@umbc.edu
Notes: 1

## Slide 2
Counters
A digital circuit usually made of flip-flops that can count the input pulse. In other words, it can generate particular outputs (called “states”) with each input clock pulse.
  Synchronous: All the flip-flops are fed by a common clock signal and their output changes simultaneously.
  Asynchronous: Usually one of the flip-flops is fed by an external clock pulse, others get the clock pulse from output of another flip-flop.
    Also called ‘ripple’ counter

## Slide 3
Counters
Asynchronous counter
Synchronous counter

## Slide 4
Counters
SYNCHRONOUS COUNTERS | ASYNCHRONOUS COUNTERS
The propagation delay is very low. | Propagation delay is higher than that of synchronous counters.
These are faster than that of ripple counters. | These are slow in operation.
Large number of logic gates are required to design | Less number of logic gates required.
High cost. | Low cost.
Synchronous circuits are easy to design. | Complex to design.
Standard logic packages available for synchronous. | For asynchronous counters, Standard logic packages are not available.

## Slide 5
Counters
Commonly used counters:
Decade counter – counts through ten states per stage
Up/down counter – counts both up and down, under command of a control input
Ring counter – formed by a shift register with feedback connection in a ring
Johnson counter – a twisted ring counter
Cascaded counter
Modulus counter.

## Slide 6
Designing Synchronous Counters
Step 1: Get the State Diagram
We’ll be using this one

## Slide 7
Designing Synchronous Counters
Step 2 : Develop Next-State Table

## Slide 8
Designing Synchronous Counters
Step 3 : Develop Flip-Flop Transition Table
  Choose your Flip-Flop
  Use corresponding excitation table
  Note that the no. of required flip-flops is the same as the no. of bits in a state.
JK flip-flop excitation table

## Slide 9
Designing Synchronous Counters
Step 4 : Develop K-Map from the transition table
 | 0 | 1
00 | 1 | X
01 | 1 | X
11 | 1 | X
10 | 1 | x
 | 0 | 1
00 | X | 1
01 | X | 1
11 | X | 1
10 | X | 1
Jo=1
Ko=1

## Slide 10
Designing Synchronous Counters
Step 5 : Realize the circuit from the function

## Slide 11
Designing Synchronous Counters
Example: Today’s Lab
  Problem: Design a counter that will display the following hexadecimal numbers in the given sequence-
    9 > 2 > A > 5 > d > 3

## Slide 12
Designing Synchronous Counters
Step 1: Develop the state diagram:
    9 > 2 > A > 5 > d > 3

## Slide 13
Designing Synchronous Counters
Step 2 and 3: Develop next-state table and transition table: We’ll be using JK flip-flop.
 |  | J3 | K3 | J2 | K2 | J1 | K1 | J0 | K0
0000 | - | X | X | X | X | X | X | X | X
0001 | - | X | X | X | X | X | X | X | X
0010 | 1010 | 1 | X | 0 | X | X | 0 | 0 | X
0011 | 1001 | 1 | X | 0 | X | X | 1 | X | 0
0100 | - | X | X | X | X | X | X | X | X
0101 | 1101 | 1 | X | X | 0 | 0 | X | X | 0
0110 | - | X | X | X | X | X | X | X | X
0111 | - | X | X | X | X | X | X | X | X
1000 | - | X | X | X | X | X | X | X | X
1001 | 0010 | X | 1 | 0 | X | 1 | X | X | 1
1010 | 0101 | X | 1 | 1 | X | X | 1 | 1 | X
1011 | - | X | X | X | X | X | X | X | X
1100 | - | X | X | X | X | X | X | X | X
1101 | 0011 | X | 1 | X | 1 | 1 | X | X | 0
1110 | - | X | X | X | X | X | X | X | X
1111 | - | X | X | X | X | X | X | X | X
State diagram
Excitation table

## Slide 14
Designing Synchronous Counters
Step 4: Obtain the function for each inputs using K-map.

## Slide 15
Designing Synchronous Counters
Step 5: Implement the functions in circuit.
  We’ll be observing the states in 7-segment display using the decoder IC.

## Slide 16
Designing Synchronous Counters
Notes:
  You can use any flip-flip e.g. SR, D or T flip-flop to design the counter.
  No. of flip-flops to be used is the same as the no. of bits in a state
  If you want to use D or T flip-flop, you can use JK flip-flop to implement them as the following-

## Slide 17
  IC 9368 for interfacing the 7-segment display:

## Slide 18
Final Assignment and Test
  It will carry 25% of the total points for the lab.
  It consists of 2 parts-
    Written assignment to be submitted at the beginning of the next lab.
    You have to make the circuit in lab that you’ll design in the assignment.

## Slide 19
Final Assignment and Test
  Written assignment: You need to design a counter. The states you need to display are assigned individually at the end of the slide.
  You need to develop the following in the assignment-
    State diagram
    State table and transition table (mention clearly which flip-flop you’ll be using).
    K-map for each flip-flop and the function for each input in terms of outputs.
    Full circuit diagram of the counter.
  ii)

## Slide 20
Final Assignment and Test
  Lab task:
    Implement your designed circuit in the lab.
    Notes:
    1. Keep a copy of your designed circuit in the lab so that you can follow it while making circuit.
    2. Be careful about the ICs you’ll be using. For JK flip-flop, check if it’s 7476 or 74112. For 7-segment display, check for IC 14495 or 9368.
    3. If your circuit doesn’t work in the lab, submit a detailed circuit diagram showing the connection for each pin. You’ll get most of your points.

## Slide 21
Questions?
Notes: 21